## Slide 1: Hands-on: Capping practice
NDCLab
Florida International University

## Slide 2: EGI capping practice
Take turns placing the EGI net on one person.
If not already prepared, help prepare the solution.
Each person should:
  Measure the participants head and confirm net to use
  Remove net from solution and gently dry
  Place the net on the participant
  Center net, tighten, recenter
    Have second person confirm alignment
  Remove net and place back in solution (for next person to practice
After everyone has practiced, help clean and disinfect the net. Clean and put away all supplies

## Slide 3: Brain Vision capping practice
Take turns placing the Brain Vision net on one person.
Each person should:
  Measure the participants head and confirm net to use
  Test the cap fit
  Insert the electrodes (only 32 for practice)
  Place the net on the participant
  Center net, tighten, recenter
    Have second person confirm alignment
  Work down all impedances
  Remove net and help clean off gel from participant
  Remove electrodes from cap and wipe off gel
After everyone has practiced, help clean and disinfect the cap and electrodes. Clean and put away all supplies